Lab 2 – TCP and UDP
TCP
1. The IP address of the sender is 192.168.1.102 and the port number is 1161
2. The IP address of the umass server is 128.119.245.12 and the port number is 80
3. The IP address of my own computer is 137.207.163.112 and the port number is 38607
4. The sequence number of the TCP SYN segment is 0. Having the second bit set in the flags section of the header identifies the segment as SYN
5. The sequence number of the SYNACK segement is also 0. The value of the acknowledgement field in this segment is 1. The umass server determined this by looking at the sequence number of the segment it was acknowledging. Having the second and fifth bits set in the flags section of the header is what identifies the segment as SYNACK
6. The sequence number of the segment containg the POST command is 148449
  //My computer crashed here, so I had to re-transmit do the file transfer. Answers my be off because of this
7. On all ACKS, I looked at the time the original segment was sent and when the ACK was received to get time sent, ACK, and RTT
Sequence #	Time sent	ACK received	RTT	Estimated RTT
148449	0.4458	0.5336	0.09	0.0922
1 (ACK)	0.3846	0.4472	0.0626	0.0902125
1 (ACK)	0.3947	0.4494	0.0547	0.0875734
1 (ACK)	0.3948	0.4527	0.0579	0.0849143
1 (ACK)	0.3949	0.4528	0.0579	0.0823775
1 (ACK)	0.3953	0.4561	0.0608	0.0800782

Number segment	Length
1	902
2	66
3	66
4	66
5	66
6	66

1. The minimum for the whole transmission is 91
2. There are no retransmitted files in the trace. I found this out by looking for a segment without an ACK
3. The receiver typically acknowledges 2986 bytes in an ACK. Each ACK is typically for every other received segment
4. The throughput is 7666.6 bits/s. I got this number via the formula Throughput = 3/4 * W/RTT = .75 * (115*8)/0.09
5. TCP slowstart begins at about 0.05s and ends at about 0.15s. After this, the pattern because linear as in TCP Reno.
6. TCP slowstart seems to start and end very quickly on my computer multiple times (0.12->0.13, 0.18->0.2, etc.). This is similar to TCP Tahoe that we learned about in class in that the transmission rate drops but then starts doubling again.

UDP
//For this, I used the trace included in the zip file
1. From the packet I chose, I would figure there are 4 fields per header. These are source and destination ports, length, and checksum.
2. The length of each header field appears to be 8 bytes long.
3. The value of the length field is the value of the UDP segment including the header.
4. The maximum number of bytes that can be included in a UDP payload is 65527 (All bits set minus header length = 65535 - 8)
5. The largest possible source port number is 65535 (All bits set)
6. UDP is protocol 17d or 0x11h
7. The source port is the destination port for the return and vice-versa