Lab 4 – ICMP and IP
ICMP
1. The IP address of my host is 192.168.1.101 and the destination IP address is 143.89.14.34
2. ICMP packets don't have source and destination port numbers because they are used to communicate between hosts and routers and not app layer processes
3. The type is 8 and the code is 0. The packet also has a checksum, identifier, sequence number, and data field. Checksum, sequence number, and identifier are all 2 bytes
4. The type is 0 and the code is 0. This also has checksum, identifier, sequence number, and data. The checksum, sequence number, and identifier fields are all 2 bytes
5. My host IP is 192.168.1.101 and the destination IP is 138.96.146.2
6. The IP protocol number would be 0x11 if ICMP sent UDP packets instead
7. The echo packet has the same fields as the ping query packets, but the data is twice the size
8. The error packet isn't the same as the query packets. It contains the IP header and the first 3 fields of the original request
9. The last 3 packets have type 0, reply, instead of 11, TTL exceeded. They're different because the requests made it to the destination
10. There is a link with long delay from New York to Pastourelle, France

IP
1. The IP address of the computer is 192.168.1.102
2. ICMP (1)
3. The are 20 bytes in the IP header and 36 in the payload (56 total – 20 header)
4. The more fragments bit is 0, so it is not fragmented
5. Identification, TTL, and header checksum change
6. The fields that stay constant are:
  1. Version – we are using IPv4 for all packets
  2. Header length – all ICMP packets
  3. Source IP – we are sending from the same source
  4. Destination IP – we are sending to the same destination
  5. Differentiated Services – all packets are ICMP
  6. Upper Layer Protocol – all ICMP packets
  The fields that must change are:
  1. Identification – IP packets must have different Ids
  2. TTL – traceroute increments with each packet
  3. Checksum – headers changes, so the checksums must too
7. The IP identification increments with each echo request
8. The identification field is 40316 and the TTL is 255
9. The identification field always changes (see question 6). The TTL stays the same because the TTL for the first hop router is always the same
10. Yes, this packet was fragmented
11. The more fragments flag is set, so it must have been fragmented. The offset is 0, so we know it's the first fragment. The first fragment has length 1500 including the header
12. The offset is 1480, so we know it's not the first fragment. The more fragments flag is 0 so we know it's the last fragment
13. The fields that changed between fragments are total length, flags, offset, and checksum
14. There were 3 packets created
15. The fields that changed are offset, checksum, total length, and flags